SHeM ray tracing simulation formatted output

Results of the SHeM ray tracing simulation are presented in a Matlab data file (.mat) and a series of images. Three images are provided per detector aperture: one with only the single scattering contribution, one with only the multiple scattering contribution, and one with the combined signal; other sources of signal that can appear in images are neglected, for example the effusive beam observed in both the Cambridge and Newcastle instruments.

The Matlab data file contains three structured data types containing the key parameters and results of the simulation. The three data structures, distances are in mm:

- im - output data and necessary information to interpret the image
  - single - cell array of the single scattering contribution for each detector
  - raster_movement_x - movement of the sample between pixels in the x direction
  - raster_movment_y - movement of the sample between pixels in the y direction
  - multiple - cell array of the multiple scattering contribution for each detector
- param - general parameters of the simulation
  - detector_position - cell array of the [x,y] coordinates of the centre of the detectors in the z=0 plane
  - detector_axes - cell array of the [x,y] axes of the elliptical detector apertures. Apertures defined as ellipses in the [x,y] plane.
  - z_sample_to_detector - the z distance from the sample to the detector/pinhole plane, can be termed the "perpendicular working distance"
  - rays_per_pixel - the number of rays per pixel used in the simulation
- beam_param - parameters that define the incident beam used
  - init_angle - (degrees) the incidence angle used
  - source_size - (radians) angular size of the virtual source size used, for the 'Uniform' model it the maximum angle gone up to, for the 'Gaussian' it is the standard deviation of the source
  - source_model - which model of the virtual source is used. 'Uniform' or 'Gaussian' currently
  - pinhole_r - radius of the pinhole
  - pinhole_c - centre of the pinhole [x, y] in the simulation coordinate system, the z coordinate is defined to be at 0